| Digital Pupillary Distance Meter (JP8) |  |
| --- | --- |
| 1.Data show range, two eyes PD-44-83mm 2.Effective measure range, two eyes PD 45-82mm Left-right PD 22.5-41.5mm 3.Minimum show equivalent,0.5mm 4.Instrument measure accurate, 0.5mm 5.Target distance, 30cm-++ 6.Power supply, dirrect Current 6V(4 AA cell) 7.Automatic shut time, about one minute after stopping use 8.One eye isolator, offer 9.Instrument size, 214x450x51 10.Instrument weight, 600g 11.Minimun show dissymmetry,0.5mm 12.Results are accurate to(within), 0.25mm |  |
| Features |  |
| Easy handling, when measuring pupil separation with the instrument, just measure the separation of distant vision, Separations for different vision distance can be obtained by calculation. All functions are obtained by full digital code operation, so the instrument is digital measuring, which is stable and reliable The instrument adopts liquid crystal digital display, with attractive and graceful appearance. Automatic shut time, about one minute after stopping using Instrument serial number mean electron coding |  |
|  | Contact Point, |
|  | Name: Oscar Fanyun Address:Rm302, No.128 North Zhangjiabang Road, Pudong District, Shanghai, P.R.China |
|  | Telfax:+86-21-58881005 |
|  | Cell:+86-(0)13524339730 |

## PD METER